## Slide 1
CICS Sample GLUE : XFCREQ
Arndt.eade@uk.ibm.com
February 2026
Arndt Eade

## Slide 2: Content
The following are described in this presentation:
An overview of CICS exits
The problem we are seeking to resolve
The solution
The artifacts
Solution alternatives

## Slide 3
Overview

## Slide 4: overview
Those familiar with the systems management of CICS TS will be aware of the ability to execute user programs at strategic points during the execution of a transaction. The intent being that user code can modify the behaviour of CICS to meet specific requirements.
CICS provides different exit types, which serve different purposes (see Customizing with user exit programs - IBM Documentation).
Global User Exits (GLUEs) are perhaps the most well known (see Global user exit programs - IBM Documentation).
This document, the scenario it describes, and the business problem it seeks to resolve use the GLUE interface at the XFCREQ exit point.
The XFCREQ exit points is driven for file control API requests before any action is taken by CICS file control; this allows the exit to modify the input parameter list, including the file name being accessed.

## Slide 5: overview
The package of programs, CICS resource and VSAM file definitions provided are sufficient to demonstrate the solution.
We have also described several modifications to the design which may better suit your scenario and will hopefully provide some additional flexibility in implementation.

## Slide 6: Terminology
Certain terms are used in this document which are described below. Clarifying their meaning will hopefully reduce ambiguity.
Application – A set of CICS resources which represent a business application. Typically made up of CICS transaction, program and data resource definitions.
TRANSACTION – A 1-4-character name of a CICS TRANSACTION definition used to initiate a business function in CICS.
PROGRAM – A 1-8-character name of a CICS PROGRAM definition. Executed as part of a transaction.
Task – a single executing instance of a transaction.
FILENAME – A 1-8-character name of a CICS FILE resource definition. Contains the name of the underlying VSAM dataset to be accessed.
DATASET – The underlying dataset name defined to z/OS. Up to 44 character in length.

## Slide 7
The problem to be solved

## Slide 8: The problem
Business applications almost always require access to data. CICS provides access to many different data sources, of which one of the most frequently used are VSAM datasets.
Without going into detail as to why VSAM datasets are used or the enhancements to VSAM which go a long way to addressing the problem described, many applications still have a requirement to periodically suspend CICS access to VSAM datasets in order that housekeeping activities can occur.
Housekeeping could be reorganisation of the files or the updating of data with information gathered outside of CICS.
This suspension of service is known as an outage and in some cases can be a daily occurrence. Clearly, for highly available applications, this has a negative impact and the ability to reduce or remove the outage is advantageous.

## Slide 9: The scenario
A finance application is accessed in CICS by invoking transaction ABCD.
Transaction ABCD may access one or more of the following four FILEs named:
  SMPFILE1, SMPFILE2, SMPFILE3 and SMPFILE4.
The four FILE definitions map to four datasets as follows:
  SMPFILE1 - FINANCE.DATASET1
  SMPFILE2 - FINANCE.DATASET2
  SMPFILE3 - FINANCE.DATASET3
  SMPFILE4 - FINANCE.DATASET4

## Slide 10
ABCD task starts
Executes initial business logic
EXEC CICS READ FILE(SMPFILE1)
Analyse data received
EXEC CICS READ FILE(SMPFILE2)
EXEC CICS READ FILE(SMFFILE4)
Execute business logic
EXEC CICS READ UPDATE FILE(SMPFILE3)
Execute business logic
EXEC CICS REWRITE FILE(SMPFILE3)
EXEC CICS WRITE FILE(SMPFILE4)
ABCD task ends

## Slide 11
ABCD task starts
Executes initial business logic
EXEC CICS READ FILE(SMPFILE1) - CICS reads from FINANCE.DATASET1
Analyse data received
EXEC CICS READ FILE(SMPFILE2) - CICS reads from FINANCE.DATASET2
EXEC CICS READ FILE(SMFFILE4) - CICS reads from FINANCE.DATASET4
Execute business logic
EXEC CICS READ UPDATE FILE(SMPFILE3) - CICS reads(update) from FINANCE.DATASET3
Execute business logic
EXEC CICS REWRITE FILE(SMPFILE3) - CICS writes to FINANCE.DATASET3
EXEC CICS WRITE FILE(SMPFILE4) - CICS writes to FINANCE.DATASET4
ABCD task ends

## Slide 12: The scenario
Currently, on a daily basis, access to transaction ABCD is disabled in order that files SMPFILE1, SMPFILE2 and SMPFILE3 can be closed in CICS, allowing a new version of the underlying datasets to be created.
Note: SMPFILE4 contains static data which does require updating on a daily basis.
FINANCE.DATASET1-3 are deleted and recreated using updates from batch processing which have been running in parallel. The exact processes involved in creating the new instances will vary from customer to customer and are not covered here. Once the process is complete, and the new datasets are ready and available, the FILENAMEs can be opened in CICS and access to transaction ABCD can resume.
Changing the FILENAME used by the application is possible but isn't generally a feasible solution. This is because most companies resist changes to application code when alternatives are available.

## Slide 13: Sequence of events
A possible sequence of events that occur during outage
IN CICS: Application disabled
  Business application no longer available to users
IN CICS: FILENAMEs SMPFILE1-3 CLOSED and DISABLED
IN BATCH: DATASETS FINANCE.DATASET1-3.NEW created (could be done prior to 1)
IN BATCH: DATASETS FINANCE.DATASET1-3 deleted
IN BATCH: DATASETS FINANCE.DATASET1-3.NEW renamed to FINANCE.DATASET1-3
IN CICS: FILENAMES SMPFILE1-3 OPENED and ENABLED
IN CICS: Application enabled
  Business application available to users
Between points 1 to 7 an application outage is occurring.

## Slide 14: Requirements of the application
The finance application has some requirements that must be observed:
When the application is disabled (1) currently running tasks must be allowed to complete normally
The application runs across multiple CICS regions and tasks in all CICS regions must complete as part of step 2.
  This has implications for VSAM RLS and non-RLS datasets, but the proposed solution works for both access types.
  Step 2 would involve a QUIESCE activity for VSAM RLS datasets
  Step 6 would involve an UNQUIESCE activity for VSAM RLS datasets
No changes to the application code or the FILENAME definitions they specify when accessing data
If multiple copies of datasets are to be used, then a single instance of a task must be consistent in which copy or set of copies they access.

## Slide 15
Proposed solution

## Slide 16: Overview of a solution
CICS FILE definitions map to a single underlying dataset as is the case for FILENAME SMPFILE1 which maps to z/OS dataset FINANCE.DATASET1.
This solution implements a mechanism whereby eligible files used by the finance application are intercepted and mapped to one of two underlying filenames. The application is unaware that this is happening thus allowing different datasets to be seamlessly removed or made available to the application.
To allow this process to occur for a group of files, the concept of a FILESET is introduced which defines a set of one or more files which must be consistent in their content. This allows a FILESET indicator to be used to determine which set of files should be used at any given time.
The XFCREQ GLUE point is used to implement this solution. Processing within the GLUE determines which FILESET to use when a task accesses its first file. The FILESET is stored for the life of the task thus ensuring a switch of FILESETs while a task is running does not cause more than one FILESET to be used.
It should be noted that multiple programs can be active at the XFCREQ exit point and that when activated the exit is invoked for ALL file control requests, irrespective of application or filename.
It should also be understood that the exit is invoked in the CICS region where the EXEC CICS file access occurs, not the CICS region where the FILE is located. This is relevant for infrastructures with AOR-FOR configurations.

## Slide 17: Processing without the exit active
ABCD task starts
Executes initial business logic
EXEC CICS READ FILE(SMPFILE1)
<Program suspends>
<Program resumes>
Processing continues
ABCD task ends
CICS FILE CONTROL invoke passing in parameters:
FILENAME
Key of record
Input/output area
Other parameters
Note: the actual file request may be routed to another CICS regions. Not before the XFCREQ GLUE has been invoked (if active in the regions).
Dataset request processed
RESPONSE RETURNED TO TASK:

## Slide 18: Changes to CICS
Changes to CICS
CICS FILE definitions REMOVED:
  SMPFILE1 - FINANCE.DATASET1
  SMPFILE2 - FINANCE.DATASET2
  SMPFILE3 - FINANCE.DATASET3
Note: SMPFILE4 remains as not part of daily housekeeping
Two sets of new FILES definitions CREATED:
  £MPFILE1 - FINANCE.DATASET1.V1 (FILESET A)
  £MPFILE2 - FINANCE.DATASET2.V1 (FILESET A)
  £MPFILE3 - FINANCE.DATASET3.V1 (FILESET A)
  #MPFILE1 - FINANCE.DATASET1.V2 (FILESET B)
  #MPFILE2 - FINANCE.DATASET2.V2 (FILESET B)
  #MPFILE3 - FINANCE.DATASET3.V2 (FILESET B)

## Slide 19: Processing with the exit active
ABCD task starts
Executes initial business logic
EXEC CICS READ FILE(SMPFILE1)
<Program suspends>
<Program resumes>
Processing continues
ABCD task ends
CICS FILE CONTROL invoke passing in parameters:
FILENAME
Key of record
Input/output area
Other parameters
XFCREQ exit called passing parameter list.
Exit program checks if first file request by task
  Checks GWA to determine FILESET to use (A)
  FILESET A saved in task specific area
Scan list of eligible files
  Find SMPFILE1 in list.
  Check FILESET to use (A)
  Changes FILE name to £MPFILE1
RESPONSE RETURNED TO TASK:
Note: Task is unaware that the request has been redirected to £MPFILE1.

## Slide 20
ABCD task starts
Executes initial business logic
EXEC CICS READ FILE(SMPFILE1) - Redirected to £MPFILE1
Analyse data received
EXEC CICS READ FILE(SMPFILE2) - Redirected to £MPFILE2
EXEC CICS READ FILE(SMFFILE4) - not in list so not redirected
Execute business logic
EXEC CICS READ UPDATE FILE(SMPFILE3) - Redirected to £MPFILE3
Execute business logic
EXEC CICS REWRITE FILE(SMPFILE3) - Redirected to £MPFILE3
EXEC CICS WRITE FILE(SMPFILE4) - not in list so not redirected
ABCD task ends

## Slide 21: notes
Multiple programs can be enabled at the XFCREQ exit point, so coexistence is necessary.
  The exit was tested with multiple programs enabled at the XFCREQ exit point
Each program enabled at an exit point can request a Global Work Area (GWA)
The GWA is defined for the total period the Exit program is enabled.
The GWA must be initialised between the ENABLE and START of the program at the exit point
For this design, the FILESET to use, the substitution character used to change the FILENAME , and the list of eligible files are all stored in the GWA.
A maintenance program is supplied to ENABLE and DISABLE the GLUE and to DISPLAY and UPDATE the FILESET in use in the GWA.
Once ENABLED and STARTED, the exit program is invoked for all file control requests in the region.

## Slide 22: How does this impact the housekeeping window
This was the before sequence of events
IN CICS: Application disabled
  Business application no longer available to users
IN CICS: FILENAMEs SMPFILE1-3 CLOSED and DISABLED
IN BATCH: DATASETS FINANCE.DATASET1-3.NEW created (could be done prior to 1)
IN BATCH: DATASETS FINANCE.DATASET1-3 deleted
IN BATCH: DATASETS FINANCE.DATASET1-3.NEW renamed to FINANCE.DATASET1-3
IN CICS: FILENAMES SMPFILE1-3 OPENED and ENABLED
IN CICS: Application enabled
  Business application available to users
From point 1 to 7 an application outage is occurring.

## Slide 23: How does this impact the housekeeping window
This is the after sequence of events
IN CICS: Applications using FILESET A (Directed to .V1 datasets by using £MPFILE definitions)
IN BATCH: DATASETS FINANCE.DATASET1-3.V2 created
IN CICS: FILENAMES #MPFILE1-3 OPENED AND ENABLED
IN CICS: UPDATE GWA to specify FILESET B (Direct by #MPFILE definitions to .V2 datasets)
        New tasks will start using .V2 files
IN CICS: £MPFILE1-3 CLOSED and DISABLED
        Tasks started prior to 4 allowed to complete normally
IN BATCH: DATASETS FINANCE.DATASET1-3.V1 now available for batch processing
Notes:
No outage is taken by the CICS application during this period.
The processing would be reversed on the following day- switch would be from .V2 to .V1

## Slide 24: Limitations of the solution
The following limitations exist with this solution:
The creation of .V1 and .V2 datasets are not dependent on each other
  This means the creation of .V2 does not require .V1 as input and vice versa
A brief time exists where both sets of files are being used, albeit by different tasks
  This must be tolerable by the application

## Slide 25
Artifacts

## Slide 26: The following artifacts are provided
More details on each are provided in the following slides
This documentation file
Assembler program SMPFCREQ (source)
  Assembler copybooks (GWAMAP, EXITDATA and UEPTSMAP)
COBOL program EXITMAIN (source)
  COBOL copybooks (GWAMAP, EXITDATA, UEPTSMAP, HEXTRAN, HEXTRANL)
DFHCSDUP input for the following definitions (split into two files, Local definitions and remote definitions)
  PROGRAM definitions for SMPFCREQ and EXITMAIN
  TRANSACTION definitions MAIN (uses EXIMAIN)
  FILE definitions for £MPFILE1-4 and #MPFILE1-4
JCL to execute IDCAMS
  Create the sample FINANCE.DATASETn.Vn
  Load files with some sample records
PLT definition for PLTPI enablement of the exit
  Note EXITMAIN requires data to be specified in the INITPARM= SIT parameter
SIT PARAMETER INITPARM

## Slide 27: SMPFCREQ
Description of the program and its control
This sample assembler program is written to be enabled at the XFCREQ EXIT POINT.
It checks a GWA is present of the expected length.
It’s important that the assembler and COBOL version of the following DSECTS/COPYBOOKS are kept in sync:
GWAMAP – Maps the Global Work Area
EXITDATA – contains constants used by EXITMAIN and SMPFCREQ to initialise and set the GWA and UEPTSTOK structures
UEPTSMAP – Maps the area of storage used by SMPFCREQ to store task specific information.
  This structure is created the first time a task issues a file control request
  The structure is key to ensuring the task uses the same FILESET for the entire period it executes.
SMPFCREQ contains numerous WTO messages to aid testing and debugging. It also contains a subroutine to display data in hexadecimal format. Most of these can be removed once alterations, testing and debugging are complete.
Details on assembling and linking of GLUEs is described in the IBM DOC.

## Slide 28: GWAPMAP
Assembler and COBOL
MAPS the GWA created as part of the EXEC CICS ENABLE PROGRAM command.
Fields are:
GWAEYE – Eyecatcher to aid debugging
GWASET – Indictor of which FILESET to use. Currently will contain ‘A’ or ‘B’
GWAFLIST – an array of 8-byte FILE names which are eligible for switching. It is recommended that the most heavily accessed files are first in the list. If a file name isn’t found in the list, the filename specified in the API command is passed unaltered to CICS file control.
GWAFLLEN – Length of the file array
GWALEN – length of the GWA structure
GWAFiLEN – the number of files in the file array.

## Slide 29: EXITDATA
Assembler and COBOL
This DESECT/COPYBOOK contains data constants used by the SMPFCREQ and EXITMAIN programs to populate the GWA and task user token structures.
Fields are:
UEPPGMNM – Program name of the sample program, checked when searching for the task token structure
UEPFSETA – FILESET A indicator
UEPFSETB – FILESET B indicator
UEPEYE – task token structure eyecatcher
GWAEYE – GWA structure eyecatcher
GWAFSETA – GWA FILESET A indicator
GWAFSETB – GWA FILESET B indicator
FILELIST – List of eligible files which is copied into the GWA as part of exit initialisation.
  It is recommended that the most heavily accessed eligible files appear at the top of the list. This will reduce to search time to locate the file.
FILELLEN – Length of the file list

## Slide 30: UEPTSMAP
Assembler and COBOL
This DESECT/COPYBOOK maps the task token structure referenced by the UEPTSTOK field in the exit parameter list.
On first entry UEPTSTOK will contain the address of EISEXITT which will contain 0. When this task token area is created, its address will be stored in EISEXITT or the chain reference by it.
See Using the task token UEPTSTOK - IBM Documentation for details on the use of this field, including use by multiple programs at the same exit point.
Fields are:
UEPNEXT – address of the next exit block in the chain
UEPPROG – name of the program owning this structure (should match the SMPFCREQ program name)
UEPEYE – Exit block eyecatcher
UEPFSET – FILESET in use by this task
UEPFCHAR – character used to replace first character of eligible file (based on FILESET)
UEPFILE – Current file
UEPNFILE – new file name after alteration based on FILESET substitution

## Slide 31: EXITMAIN
Program to perform exit enable, disable, display and update
This sample program can be invoked via a console, 3270 display or directly via the PLT.
If invoked by PLT, an INITPARM SIT parameter must be specified for the EXITMAIN program.
The program accepts commands:
ENABLE <FILESET>
DISABLE
DISPLAY
UPDATE <FILESET>
FILESET is a single character ‘A’ or ‘B’
The exit will issue status messages and write to a TS queue call EADEDIAG.

## Slide 32: EXITMAIN
Invoking the program
Invoking as part of PLTPI processing
ENABLE A – Will enable the exit and initialise the GWA to use FILESET A
ENABLE B - Will enable the exit and initialise the GWA to use FILESET B
Invoking via console command
F <CICSNAME>,MAIN ENABLE A - Will enable the exit and initialise the GWA to use FILESET A
F <CICSNAME>, MAIN ENABLE B -Will enable the exit and initialise the GWA to use FILESET B
F <CICSNAME>, MAIN DISABLE - Will STOP and DISABLE to EXIT
F <CICSNAME>, MAIN DISPLAY - Will DISPLAY the current FILESET in use by the exit
F <CICSNAME>, MAIN UPDATE A - Will UPDATE the GWA to use FILESET A
F <CICSNAME>, MAIN UPDATE B - Will UPDATE the GWA to use FILESET B
Invoking via 3270
MAIN <parameters> - the same parameters as specified via the console

## Slide 33: CSD LOCAL
DFHCSDUP input for the FOR regions
Contains local file definitions for the six files used in this example.
The DSNAME values should be changed to name which conform to your site standards.
If the exit and file in the same CICS region, these definitions should be installed.

## Slide 34: CSD-REMOTE
DFHCSDUP input for the local AOR CICS Region where the EXIT will run
Contains the program and transaction definitions for the exit and maintenance programs.
This file also contains remote definitions used in an AOR-FOR configuration. The REMOTESYSTEM name of the FOR will need to be changed to match your configuration.
If the exit and files are to reside in the same CICS Region, the FILE definitions in this file should not be used.

## Slide 35: FILES
DFHCSDUP input for the local AOR CICS Region where the EXIT will run
Contains the program and transaction definitions for the exit and maintenance programs.
This file also contains remote definitions used in an AOR-FOR configuration. The REMOTESYSTEM name of the FOR will need to be changed to match your configuration.
If the exit and files are to reside in the same CICS Region, the FILE definitions in this file should not be used.

## Slide 36
Solution alternatives

## Slide 37: Some potential changes to meet alternative requirements
More than two FILESET solution
The proposed solution uses substitution of the first character of the FILENAME to derive the new FILENAME
Two possible values are available determined by the GWAFSET, with UEPFCHAR providing the substitution value.
The following is possible:
Any number of FILESETs representable by a single character (A,B,C,D for instance)
Not using a substitution character, rather extend the GWAFLIST so that each entry, rather than a single file name, represents the FILENAME, FILENAME FILESET(A), FILENAME FILESET(B), etc, etc
  This would allow greater flexibility in the filenames used.
  SMPFILE1-> £MPFILE1 or #MPFILE1 becomes SMPFILE1,ABCFILE1,DEFFILE1

## Slide 38: Some potential changes to meet alternative requirements
More than two FILESET solution
A slight variation of the two FILESET solution whereby two different underlying FILENAME definitions are defined, both of which are different to the FILENAME passed in by the application, is to have one of the underlying FILENAME definitions the same as the FILENAME passed in. This means that should the XFCREQ exit not be enabled, the application request will effectively default to the FILENAME specified in the application program.
This would add flexibility as to when the exit is enabled and allow the application to continue to run irrespective of the exit status.

## Slide 39: Some potential changes to meet alternative requirements
Timestamp switching
Use of the UEPTSTOK and EISEXITT fields to ensure each task uses only one FILESET resolved consistently at the UOW and task level. The solution does however mean that at any point in time two tasks could use different FILESETs if a switch occurs between the time task#1 first accesses a file and task#2 first accesses a file.
Consideration was given to using a reference time which would force tasks that start before the reference time to use one FILESET, while those started after the reference time used a new and different FILESET. This solution will require more complex internal processing to implement given the initial values in the EIB (EIBDATE/EIBTIME) can be altered by using an EXEC CICS ASKTIME request.
The EXEC CICS INQUIRE ASSOCIATION STARTTIME() will return the task start datetime in the format : YYYYMMDDHHMMSS.NNNNNN (20260209092610.658039 for example)
This could be extracted and compared to a similarly formatted time specified in the GWA such that:
If task start time < GWA time, use FILESET A otherwise, use FILESET B